## Slide 1
Exercise 1: Hands on CWatM
Peter Burek, Mikhail Smilovic
International Institute for Applied Systems Analysis
Research Scholars at
Water Program

## Slide 2: Hands on CWatM
Running CWatM for the first time
Run CWatM with a settings file
Test the options –l , -t
Take a look at the settings file
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 3: Hands on CWatM
0. Folder structure
Your folder structure should like this:
Root folder:
It does not matter if your
root folder has whitespace or any other strange characters
We are using relative paths!
Extract here
Exercise 4: put global climate from ftp here
Extract here
Exercise 5: put global climate from ftp here
Extract here
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 4: Hands on CWatM
0. Running batch files
  Go to folder CWATM_exercise1
  Start: 01_exe_example.bat or open a DOS command prompt
  - press Windows+R
  - type cmd + return
  - change directory: e.g.: cd c:/CWATM/CWATM_exercise1 (or cd “c:/directory with white space/CWATM/CWATM_exercise1”)
  Type ..\CWATM_model\CWatMexe\cwatm.exe
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 5: Hands on CWatM
Running CWatM for the first time
  Go to folder CWATM_exercise1
  Start: 01_exe_example.bat
  Or use the command line (slide before)
  cd c:/CWATM/CWATM_exercise1 ..\CWATM_model\CWatMexe\cwatm.exe
CWAT_exercise1
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 6: Hands on CWatM
2. Run CWatM with a settings file
  Start 02_exercise.bat ../CWATM_model/CWatMexe/cwatm.exe settings_rhine30min.ini –l
  Use a text editor e.g. notepad, textpad, notepad++
  Look at ./output/discharge_daily.tss
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 7: Hands on CWatM
3. Run CWatM with a settings file
  Start 03_exercise.bat ../CWATM_model/CWatMexe/cwatm.exe settings_rhine30min.ini –l -t
  Use a text editor e.g. notepad, textpad, notepad++ to change 03_exercise.bat
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 8: Exercise 3: Hands on CWatM
4. Take a look at the settings file
  Change settings_rhine30min.ini with a text editor
  Look for gauges in settings_rhine30min.ini
  Change it to Gauges = 6.25 51.75 7.75 49.75
  Change StepEnd = 100
  Start 02_exercise.bat
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 9: Hands on CWatM
9. Homework
Play around with the Rhine catchment change the settings file: settings_rhine30min.ini
  Run for different times
  Produce different outputs
What catchment are you interested?
  Find out the coordinates (lat/lon) of the outlet point
  Find out coordinates of gauges
  Send me the coordinates for next lesson
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 10
Problems
Most problems come from different file systems, folder structures
We try to set up everything with relative path.
Please make sure that your folders have a similar structure like in slide 3 in cwatm_exercise1.ppt
The settings file has a part:
[FILE_PATHS]
PathRoot = ../cwatm_data ../ jumps back to the previous folder
PathOut = ./output ./ uses the folder output in the same folder as the settings file or the directory you are in
PathMaps = $(PathRoot)/cwatm_input30min
PathMeteo = $(PathRoot)/climate/rhine
3. If this is not working you can use also absolute path (also with white space)
PathRoot = C/root directory/second.root/cwatm/cwatm_data
4. If you execute cwatm you can also use absolute path
instead
../CWATM_model/CWatMexe/cwatm.exe settings_rhine30min.ini –l
“C/root directory/second.root/cwatm/CWATM_model/CWatMexe/cwatm.exe” settings_rhine30min.ini –l (mind the “ if there are white spaces)
5. Some other errors we address in:
https://cwatm.iiasa.ac.at/tutorial.html#test-the-python-model-version
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.