## Slide 1
Exercise 5: Higher resolution
Peter Burek, Mikhail Smilovic, Luca Guillaumot
International Institute for Applied Systems Analysis
Research Scholars at
Water Program

## Slide 2: Higher resolution – 5 arcmin
0. What you need – downloading data from FTP
The world at 30 arcsec
Example for River Rhine, Central Europe
Example for Lake Tana, Blue Nile, Ethiopia
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 3: Higher resolution - 5 arcmin
0. What you need
You downloaded already the climate data (precipitation, temperature, radiation etc.) from ftp climate_2011_2012.zip or even wfdei.tar
You need a global dataset on 5 arcmin please download:
cwatm_input5min.zip from ftp
please copy to the folder CWATM_data and unzip (extract here) in
CWATM_data/cwatm_input5min
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 4: Higher resolution - 5 arcmin
2. The world in 5 arcmin raster
CWatM is a distributed model which can be used at different resolutions e.g. 30 arcmin, 5 arcmin, 1km
This is a part of the World (Ethiopia) split into 5 arcmin cells (around 10 km x 10 km)
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 5: Higher resolution - 5 arcmin
3. Flow accumulation map
upstream catchment area of each cell in km2
See upstream_area_5min_km2.tif
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 6: Higher resolution - 5 arcmin
4. Upstream area of lake Tana
Lake Tana, 5 arcmin resolution
Lake Tana, Ethiopia
Real location of outlet of lake Tana
and 5 arcmin network outlet
Flow accumulation Lake Tana till conjunction Blue Nile with White Nile
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 7: Exercise: Higher resolution - 5 arcmin
1. Run 5 arcmin for the Rhina basin
Folder: CWATM_exercise5
Based on the Rhine basin:
Run:
..\CWATM_model\CWatMexe\cwatm.exe settings_rhine_5min_51.ini -l
Or: 51_exe_rhine_example.bat
Important!
We are in folder CWATM_exercise5
Please cd CWATM_exercise5
but we using the model stored in CWATM_model
Folder structure CWATM_exercise5
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 8: Exercise: Select a basin
2. Select another outlet of a basin
Based on the Rhine basin:
Change a few line in the setting: settings_rhine_5min_51.ini
And save it with the name: settings_tana_5min_52.ini
PathOut = ./output_tana Change output destination
MaskMap = 37.39 11.6
Gauges = 37.39 11.6
This will change the basin from Rhine to Lake Tana
You can use the ‘#’ to out comment a line and to keep in mind the original version!
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 9: Exercise: Select a basin
2. Select another outlet of a basin
Run:
..\CWATM_model\CWatMexe\cwatm.exe settings_tana_5min_52.ini -l
Or: 52_exe_tana_example.bat
in case you did not manage, we prepared a settings file with the changes
..\CWATM_model\CWatMexe\cwatm.exe settings_tana_5min_52.ini –l
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 10: Exercise: Select a basin
3. Select another outlet of a basin
Tana basin
Basin area fits better than with 30arcmin
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 11
Problems
Most problems come from different file systems, folder structures
We try to set up everything with relative path.
Please make sure that your folders have a similar structure like in slide 3 in cwatm_exercise1.ppt
The settings file has a part:
[FILE_PATHS]
PathRoot = ../cwatm_data ../ jumps back to the previous folder
PathOut = ./output ./ uses the folder output in the same folder as the settings file or the directory you are in
PathMaps = $(PathRoot)/cwatm_input30min
PathMeteo = $(PathRoot)/climate/rhine
3. If this is not working you can use also absolute path (also with white space)
PathRoot = C/root directory/second.root/cwatm/cwatm_data
4. If you execute cwatm you can also use absolute path
instead
../CWATM_model/CWatMexe/cwatm.exe settings_rhine30min.ini –l
“C/root directory/second.root/cwatm/CWATM_model/CWatMexe/cwatm.exe” settings_rhine30min.ini –l (mind the “ if there are white spaces)
5. Some other errors we address in:
https://cwatm.iiasa.ac.at/tutorial.html#test-the-python-model-version
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.